PROJECT PLANNING WORK SHEET

Drill Press Project

# OPERATION				TOOLS			CS/RPM

| Cut bar stock to size, deburr both parts | Combination square and power hacksaw. | SFPM |
| --- | --- | --- |
| Layout part according to blueprint. | Height gauge, combination square, scribe, and center punch |  |
| Center drill hole #1 | #4 center drill | 600 RPM to 1000 RPM |
| Drill 23/64 thru hole for reaming. . | 23/64 drill (.3594) | = 668 RPM |
| Ream 3/8 hole | .375 reamer | =427 RPM |
| Center drill hole #2 | #4 center drill | 600 RPM to 1000 RPM |