NAME: _______________________

DRILL PRESS PROJECT

INSPECTION SHEET

Hole #1 .375 Reamed hole

1. Location centered, .50 from reference end    ____________

2. .375 +.005					   ____________

3, Good surface finish			`	   ____________

4. Deburred both sides			   ____________

Hole #2  3/8-16 UNC tapped hole

1, Location centered, 1.50 from reference end   ____________

2, Good threads through			    ____________

3. Bottom deburred				    ____________

Hole #3 Drill and Counterbore for #10 Socket Head Cap Screw

1. Location centered, 2.50 from reference end   ____________

2. Counterbore Diameter.375 + .005		    ____________

3. Counterbore depth.200 + .010		    ____________

4. Thru hole correct drill size .221		    ____________

5. Both sides deburred			`	`   ____________

# Hole #4 Drill and Countersink for #10 flat head screw

1. Location centered 3.50 from reference end    ____________

2. 82 deg Countersink diameter .400-.420	    ____________

3. Thru hole correct drill .203			    ____________

4. Bottom deburred				    ____________

Overall appearance clean, deburred, free of chips    ____________

# Project Planning Worksheet

1.  All steps and operations in correct order	    	_________

2.  Clear, concise descriptions of operations	    	_________

3.  All calculations present and correct		_________

4.  Neat and well organized				_________