PROJECT PLANNING WORK SHEET

# OPERATION				TOOLS			CS/RPM

| Drill 5/16 thru hole for 3/8-16 tap | 5/16 HS Drill (.3125) | = 768 RPM |
| --- | --- | --- |
| Tap 3/8-16 threads thru | 3/8-16 tap, tap wrench, and spring loaded tap guide | Hand operation |
| Center drill hole #3 | #4 center drill | 600 RPM to 1000 RPM |
| Drill thru hole for 10-32 socket head cap screw | #2 drill (.221) | =1086 RPM |
| Cut .375 counterbore for 10-32 socket head cap screw. | .375 counterbore with .218 pilot | =533 RPM |
| Center drill hole #4 | #4 center drill | 600 RPM to 1000 RPM |
| Drill thru hole for 10-32 flat head screw | 13/64 drill (.203) | =1182 RPM |
| Countersink for 10-32 flat head screw | 82 degree 1/2 countersink | =285 RPM |
| Clean, deburr all holes and edges | 82 degree countersink and file | Hand operation and slowest speed |